# Firewall Laboratory – Module 11 Firewalls

Background:  This Lab reinforces the concepts of firewalls by requiring the student to complete the configuration of a host-based firewall.

Requirements/assumptions:

- Windows NT 4.0/2000

- Internet access

- Local administrative privileges

Scenario:  Some of the current IT staffers from RHS saw postings in an Internet chat room from an alias that the terminated employee used.  The postings were bragging about the prospects of the conquest of a newly merged company’s infrastructure by Trojans he had put in place prior to leaving the company.  It is believed that this former employee made these posts, and that he has in fact placed some malicious software somewhere on the network.  It is also believed, based on a complete scrub of the former employee’s system, that this staff member may have had knowledge and experience with the following Trojans:  SubSeven, WinCrash, and BackOrifice.  In addition, there is concern that there should be steps taken to reduce the ability to footprint the entire network through ping sweeps, both to internal and external hosts.  Only the management network, which resides in the 192.168.30.240 - 192.168.39.254 range, should be allowed to ping the hosts on the network.  All other ping requests should be dropped.

Given the short time frame for integration of the infrastructures, the CIO has made a decision to press ahead as soon as possible with the integration work.  However, to preserve security, he has directed that host-based firewalls be installed on systems that would cause the most damage to the organization if they were compromised.  Also, given the tight budget for the current fiscal year and the large number of servers that will have to be protected against the potential malicious software, you have decided that a free software tool is the only answer.  You have researched the known freeware host-based firewalls and determined that Tiny Personal Firewall is the best solution for your needs.

# Download and Install Tiny Personal Firewall

- Open the InfoSec Course Shared\Tools folder located on your Desktop

- Double Click the Tiny Personal Firewall Setup file: [pf2.exe].

- The Tiny Personal Firewall Setup Wizard starts, click the following buttons

- When the computer reboots, Tiny Personal Firewall will be running.  As various programs attempt to make connections either into or out from your system, Tiny will prompt you for input.   These may include programs such as Norton Antivirus, Internet Explorer or Netscape Navigator, etc.  Each new connection will result in a prompt that you must either permit or deny.   Ensure that you read each prompt carefully, and click the checkbox

- After you have gone through all of the initial installation steps and gone through the connections which your computer is attempting to make and either permitted or denied them, it is time to customize our rules.

- Double click on the Tiny Personal Firewall icon () in the system tray.

- Click on the ‘Advanced’ button.

- A window similar to this one will then open:

- To add the rules to block the ports, click on the ‘Add’ button.

- The following window opens up:

- You will want to configure the firewall to block the following TCP ports:  6711, 6712, 6776, 7000, 16660, 31337, 31338.  To accomplish this, perform the following steps:

  - First, give the rule a name (i.e. subseven)

  - Select from the drop down menu the protocol which this rule will apply to (i.e. TCP for subseven)

  - Select the direction from the drop down menu for the rule (Incoming)

  - Select the Port Type from the drop down menu (List of ports for subseven)

  - In the ‘List of Ports’ box, fill in those ports associated with Subseven (6711, 6712, 6776, 7000)

  - Select the appropriate action for this rule (Deny)

  - Since we’re concerned about insiders on the network, it is advisable to log when this rule is enforced (for tracking purposes and to possibly find any impropriety.  When we are through with the filter rule configuration, it should look like this:

- Now you will want to configure the firewall rules to include blocking the TCP ports for WinCrash (2583, 3024, 4092, 5742) and Back Orifice (31337-31338).  Follow the same steps above and deny all incoming traffic on those ports.

- To disable echo replies to all but the management network, start by creating a new Filter Rule (click Add… in the Firewall Configuration window)

- Enter ‘Allow Echo Request from Mgt Network’ for the description.

- Set Protocol to ‘ICMP’

- Set Direction to ‘Incoming’

- Ensure ‘Echo Request’ is in the box next to ‘Set ICMP’

- Set the remote endpoint to ‘Network/Range’

- Enter the network range (192.168.30.240 to 254)

- Click ‘OK’

- Click ‘Add…’

- Enter ‘Allow Echo Reply to Mgt Network’ for the description.

- Set ‘ICMP’ as the protocol

- Change direction to ‘Outgoing’

- Click the ‘Set ICMP’ box

- Check the box for ‘[0] Echo Reply’

- Uncheck the box for ‘[8] Echo Request’

- Click OK

- Change Remote endpoint to ‘Network/Range’ and enter the range again

- Click OK

- Test your firewall by pinging your partner’s IP address.  You should not get a response.  Then the instructor will ping all systems from a computer in the management network.  These packets should traverse the network unobstructed.