| HINTS | LAYER | NUMBER | CHARACTERISTICS | ENCAPSULATION PROCESS – PDU* | PDU HINTS | EQUIPMENT USED |
| --- | --- | --- | --- | --- | --- | --- |
| Away | Application | 7 | Closest to user Provides network service to applications (browser, email, etc) |  |  |  |
| Pizza | Presentation | 6 | Data representation Data readability and format Ensures data arriving from network can be used by the application Encryption and encoding occur here Compression and Decompression |  |  |  |
| Sausage | Session | 5 | Inter-host communication Establishes/manages/terminates sessions btn. Applications Manages dialog between parties i.e. making sure that the previous request has been fulfilled before the next one is sent class of service |  |  |  |
| Throw | Transport | 4 | Transportation issues btn hosts – TCP: connection oriented protocol that provides full-duplex (send/receive) data transmission Establish/maintain/terminate virtual circuits Fault detection and recovery Information flow control Segmentation Sequencing Windowing Assembly End-to-end connections | Segments | Some |  |
| Not | Network | 3 | Connectivity and path btn 2 end systems Routing Network address and best path IP, IPXX, and Appletalk located here | Packets | People | Network address Router |
| Do | Data Link | 2 | Access to media Reliable transfer across media Physical addressing – MAC addressing Networking topology | Frames | Fight | MAC address: Bridge NIC card switch |
| Please | Physical | 1 | Deals with data in bits (binary transmission); sending and receiving bits from the connecting medium Wires, connectors, voltages, data rates Encoding and Decoding | Bits | Back | Bits Wire (fiber, CAT-5, coaxial) Repeaters Hubs transceiver |

OSI continued:

- OSI reference model is a descriptive network scheme whose standards ensure greater compatibility and interoperability between various types of network technologies

- Contains 7 layers:  see previous page

- First 4 layers:	Host layers; concerned with end-to-end connections

- Last 3 layers:	Media Layers; concerned with media access

- Encapsulation:  the process in which data is wrapped in a particular protocol header before it is sent across the network; encapsulation creates a PDU (protocol data unit)

- During Peer-to-Peer communications, each layer’s protocol exchanges information--called PDU’s

Comparison of OSI and TCP/IP:

| OSI LAYER |  | TCP/IP LAYER |
| --- | --- | --- |
| Application |  | Application – Combines layers 5+ 6 + 7 |
| Presentation |  |  |
| Session |  |  |
| Transport | SAME | Transport |
| Network | new name | Internet |
| Data Link |  | Network Access – Combines layers 1 + 2 |
| Physical |  |  |

TCP/IP

Protocols used by TCP/IP:  SMTP,  FTP,  DNS

Protocol – a formal description of a set of rules and conventions that govern how devices on networks exchange information