2950 Switch Config

Use the following steps to configure the switch with an IP address and SNMP configurations:

- Switch>enable

- Switch# Config t

- Switch(Config)#int vlan1

- Switch(Config-if)ip address 192.168.1.2 255.255.255.0 (address and mask my different depending on the configuration scenario)

- Switch(config-if)no shut

- exit

- Switch(config)snmp-server community public

- Switch(config)snmp-server-location 192.168.1.10 (the location address might be different depending on the configuration scenario).