TCP/IP Exercise

- Launch Ethereal and start capturing packets (turn the transport layer translation off).  Connect to a web server and browse some pages as you continue to capture.

- Stop capturing and build a filter to capture packets with the IP flag Syn set (to 1), and the Ack flag set (to 0).  Apply the filter.  Open a frame and answer the following questions:

  - What is the source IP address______________________

  - What is the destination IP address_____________________

  - What is the source Port Number_______________________

  - What is the destination Port Number___________________

  - Which flags have been set:______________________________

  - What is the size of the sequence number field_______________________

  - What is the value of the sequence number field______________________

  - What is the value if the window size___________________. Is this value in bit or bytes___________________

  - What is the size of the len filed____________________

  - What is the value of the len field__________________.  What does this value mean.________________________________________________?

  - What does MSS stand for __________________.  And what is its size___

- Capture all frames that belong to the session.  (Use the follow stream feature, then apply the filter).

- Study the TCP frames using the details view and explain what evidence they provide about the following:

  - TCP handshakes
____________________________________________________________

  - TCP Acknowledgments
____________________________________________________________

  - TCP segmentation and segment size
____________________________________________________________

  - TCP sequence numbers
____________________________________________________________

  - TCP sliding windows
____________________________________________________________

  - HTTP protocol
____________________________________________________________

- Write down the syntax of the filter. _________________________________________________________________Save the filter (in text format) as “handshakes)

- Reset the filter and build a new filter to capture packets with both the IP flags Fin and Ack set to (1) and with destination host equals the local machine.

- Reset the filter and build a new one to filter packets with a segment length of 200 bytes or bigger.  
__________________________________________________________________

For further information on filters read the tcpdump manual page at http://www.tcpdump.org/tcpdump_man.html  for the windump syntax.