INTERNETWORKING I

(SEMESTER 1)

STUDY GUIDE FOR CHAPTER 1

- How is a PC similar to a network?

Both have internal components, which are connected by some type of medium (cable VS bus).

- What are three examples of out-going ports on a PC?

## Serial, parallel, and mouse

- What do notebooks and laptops use for NICs, modems, etc.?

# PCMCIA slot/card

- What is a NIC? What should you consider when buying a NIC for your computer?

Network Interface Card (also called a LAN adapter) provides communication capabilities to and from a PC.

Make sure you get the right NIC for the right cable connector (RJ-45 VS BNC)

- In Windows 95, where do you go to configure the TCP/IP settings?

# Go to the Control Panel, then Network

- What is a plug-in?

They are application programs that run proprietary files that Web browsers are unable to interpret.

- What are some things you should check when troubleshooting a PC or network? In what order should you do these things?

User

Network connection

Hardware

Software

- What is the definition of a protocol? How do networked devices use them (be general)?

A formal description of a set of rules and conventions that govern how devices on a network exchange information.

- What is a LAN? What defines a network as a LAN?

Local Area Network. They operate within a limited geographic area, allow many users access to high bandwidth, provide full-time connectivity, and connect physically adjacent devices.

- What is a WAN? What defines a network as a WAN?

Wide Area Network. They cover a large geographic area (cities, countries).

- What was one problem with WANs in the early days?

They did not use the same protocols so they couldn’t “talk” to each other. They were incompatible.

- How is binary represented in the computer world? (Give three examples)

0 or 1

Voltage or no voltage

0 volts or +5 volts

- On what numbering system is binary based on?

2

- On what numbering system is decimal based on?

10

- What is the definition of bandwidth?

The measurement of how much information can flow from one place to another in a given amount of time.

- How is bandwidth measured?

Bits per second (bps)

- Is bandwidth infinite? Why or why not?

No, it is limited by technology and the laws of physics.

- What are three things that need to be considered when you send a file over a network?

How big is the file (file size)

The available bandwidth

## The available throughput

- Why is bandwidth important?

It is important because the more bandwidth you have, the more data can be sent and can be sent quicker. It is a key component of any network.