CCNA2 Skills-Based Assessment

Notes

The physical arrangement and cabling of the routers and interfaces will be the same as it is for the standard CCNA3.0 three-router lab.

NETLAB shows a serial connection between R1 and R3. As the topology illustrates above, we will not configure or enable that connection for this exercise.

Depending upon the router model, the interfaces may differ. Example: On your router, Serial0 may be Serial0/0 and Ethernet0 may be FastEthernet0/0. Use the appropriate commands to view your hardware type.

Maximum time allowed to complete the exam is 110 minutes.

Objectives

Basic Router Configuration

Routing Configuration

Access Control List Configuration

Access Control List Verification

Preconfigs

The following items should be pre-configured on all three routers:

Hostnames on all routers

IP addresses and interface descriptions on all interfaces

All configured interfaces enabled

- Clock rates on DCE interfaces

The topology cabling

The console, vty and privilege passwords on routers

IP host tables configured

Following are the preconfigs:

Router R1

hostname R1

!

enable secret class

!

ip host R2 172.16.1.2 172.16.2.1 172.16.20.1

ip host R3 172.16.2.2 172.16.30.1

!

interface FastEthernet0/0

description R1 LAN

ip address 172.16.10.1 255.255.255.0

no shutdown

!

interface Serial0/0

description WAN link to R2

ip address 172.16.1.1 255.255.255.0

clockrate 56000

no shutdown

!

ip classless

!

line con 0

exec-timeout 0 0

password cisco

logging synchronous

login

line aux 0

line vty 0 4

password cisco

login

Router R2

hostname R2

!

enable secret class

!

ip host R1 172.16.1.1 172.16.10.1

ip host R3 172.16.2.2 172.16.30.1

!

interface FastEthernet0/0

description R2 LAN

ip address 172.16.20.1 255.255.255.0

no shutdown

!

interface Serial0/0

description WAN link to R1

ip address 172.16.1.2 255.255.255.0

no shutdown

!

interface Serial0/1

description WAN link to R3

ip address 172.16.2.1 255.255.255.0

clockrate 56000

no shutdown

!

ip classless

!

line con 0

exec-timeout 0 0

password cisco

logging synchronous

login

line aux 0

line vty 0 4

password cisco

login

Router R3

hostname R3

!

enable secret class

!

ip host R1 172.16.1.1 172.16.10.1

ip host R2 172.16.1.2 172.16.2.1 172.16.20.1

!

interface FastEthernet0/0

description R3 LAN

ip address 172.16.30.1 255.255.255.0

no shutdown

!

interface Serial0/1

description WAN link to R2

ip address 172.16.2.2 255.255.255.0

no shutdown

!

ip classless

!

line con 0

exec-timeout 0 0

password cisco

logging synchronous

login

line aux 0

line vty 0 4

password cisco

login

Configuration Tasks

Basic Router Configuration

Using the Preconfigs above, configure the three routers.

You should verify direct connections between all interfaces before continuing.

Add two loopback interfaces (loopback0 & loopback1) to router R2. These loopback interfaces will function as virtual devices in this exercise. These devices will be referred to as R2L0 and R2L1 for clarity.

The syntax of commands for configuring a loopback interface:

R2(config)#interface loopback number

R2(config-if)#ip address ip-address subnet-mask

Give R2L0 the IP address of 172.16.21.1/24.

Give R2L1 the IP address of 172.16.22.1/24.

Add one loopback interface to router R3. This loopback will function as a virtual device. This device will be referred to as R3L0.

Give R3L0 the IP address of 172.16.31.1/24

Routing Configuration

Enable IGRP on all three routers to route all network traffic. Show and analyze the routing table to ensure IGRP is working correctly.

Test connectivity from R1 to R3.

From R3L0, test ping and telnet connectivity to R2L0 and R2L1.

Access Control List Configuration

Create a named access-list that denies telnet and ping from R3L0 to R2L0 and R2L1. (You might think of this as blocking a student workstation, R3L0, from telnet and ping to your file servers, R2L0 and R2L1.)

You should always be able to telnet and ping to the serial interfaces on router R2 from any source.

You should also be able to telnet and ping to R2L0 and R2L1 from any source other than R3L0.

Access Control List Verification

Verify each configured access list to ensure that the appropriate traffic is blocked, while other traffic is permitted.

Use the ip telnet source-interface command for verifying the access list.

  - Use this command to set the IP address of an interface as the source for all Telnet connections. If the specified interface is not up, the Cisco IOS software selects the address of the interface closest to the destination as the source address. This command is applied in the Global configuration mode.

    - The syntax for this command is: ip telnet source-interface interface

  - Example: The following example forces the IP address for FastEthernet interface 1 as the source address for Telnet connections:

    - Router(config)# ip telnet source-interface FastEthernet1

  - To reset the source address to the default for each connection, use the no form of this command.

    - The syntax for this command is: no ip telnet source-interface

The following table is provided for you to document your testing for your confirmation. If the access list fails to control the traffic, consider revising the configuration(s).

| Packet Type | From Router/Interface | To Router/Interface | Results |
| --- | --- | --- | --- |
| Ping | router R3/Loopback0 | router R2/Serial0 | success |