# !!!!!!!!!! Begin copy and paste !!!!!!!!!!!!!!!!!!

# hostname GAD

# enable secret cisco

# interface Serial0/0

# description this is the DCE serial interface connected to Anniston's S0/0

# ip address 192.168.2.1 255.255.255.0

# clock rate 64000

# no shutdown

# exit

# interface Serial0/1

# description this is the DCE serial interface connected to Boaz's S0/0

# ip address 192.168.102.1 255.255.255.0

# clock rate 64000

# no shutdown

# exit

# ! This is to simulate an intranet web server host that everyone can access !

# interface lo 0

# ip address 172.16.0.1 255.255.0.0

# exit

# ! this is to simulate a server pool !

# ! upper servers can only be reached by management pcs !

# ! lower servers can be reached by any pc !

# interface lo 209

# ip address 209.0.0.1 255.255.255.0

# ip address 209.0.0.254 255.255.255.0 sec

# exit

# ! this is to simulate a random host on the Internet to be used to check general access !

# interface lo 62

# ip address 62.0.0.1 255.0.0.0

# exit

# ! This is to simulate an internet host that needs to be banned from being reached by any host !

# interface lo 198

# ip address 198.0.0.1 255.255.255.0

# exit

# ! this is to start the web server to simulate external networks !

# ip http server

# ! these are the configurations for the RIP process !

# router rip

# network 192.168.2.0

# Network 192.168.102.0

# network 172.16.0.0

# network 209.0.0.0

# network 62.0.0.0

# network 198.0.0.0

# exit

# !!! make sure to do a copy running-config startup-config !!!!