InterVLAN Routing and 802.1Q Trunking On Catalyst 2950 Switches
 Using AN External 2620/2621 Router

- Consol into both switches and erase them.  Name the first switch SwitchA, and the second switch SwitchB.  Refer to previous labs if necessary.

- Set switchA as the VTP server.

- On switch A, create three VLANs—VLAN 2, 3, and 4.  Name VLAN 1 Admin, VLAN 2 Accounting, VLAN 3 Marketing, and VLAN 4 Sales.   Refer to previous labs for steps and configuration commands if necessary.

- Assign port 2 to VLAN 2, Port 3 to VLAN 3, and port 4 to VLAN 4.  Refer to previous labs for steps and configuration commands if necessary.

- Set SwitchB as a VTP domain Karl Client

(Notice that domain name (Karl) is case sensitive and must be typed exactly as shown.  Also, you must assign the domain name before you make a switch a VTP client.  If the VTP client command is typed first, the domain name cannot be set.

- Connect a crossover cable between port fa 0/10 on both switches on the 2950 switch

- Create trunk ports on both switches.  Refer to previous labs for steps and configuration commands if necessary.

- On SwitchB, assign port 2 to VLAN 2, Port 3 to VLAN 3, and port 4 to VLAN 4.  Refer to previous labs for steps and configuration commands if necessary

- Erase the configuration file on the router, and reload

- Name the router Central_Office

- Connect a straight through cable from fa 0/0 on SwitchA to fa 0/0 on the router.

- Select FastEthernet 0/0 for the trunk configuration using the following Commands:

Central_Office(config)#int fa 0/0

Central_Office(config-if)# no shut

Central_Office(config-if)#exit

- Enable Trunking on the sub-interfaces 0/0.1, 0/0.2, 0/0.3, and 0/0.4, using encapsulation dot1q, and configure layer 3 information on the sub interfaces using the following commands:

Central_Office(config)#int fa 0/0.1

Central_Office(config-subif)#encapsulation dot1q 1

Central_Office(config-subif)#IP address 192.168.1.1 255.255.255.0

Central_Office(config)#int fa 0/0.2

Central_Office(config-subif)#encapsulation dot1q 2

Central_Office(config-subif)#IP address 192.168.2.1 255.255.255.0

Central_Office(config)#int fa 0/0.3

Central_Office(config-subif)#encapsulation dot1q 3

Central_Office(config-subif)#IP address 192.168.3.1 255.255.255.0

Central_Office(config)#int fa 0/0.4

Central_Office(config-subif)#encapsulation dot1q 4

Central_Office(config-subif)#IP address 192.168.1.1 255.255.255.0

- Save your running-configuration file

- Configure the router with RIP

- Use the command show vlan , and show interface, and show IP route on the router to check on your configuration.

- On SwitchA connect a host to port 2, and assign the proper IP address, subnet mask, and default gateway.

- On SwitchB connect a host to port 3.  And assign the proper IP address subnet mask, and default gateway.

- Ping between the two hosts.  Was the ping successful? ________.  If not troubleshoot

____________________Instructor’s Initial