1900/2950 Switch VLAN Trunking

Objective:

Be able to create a trunk on 1900/2950 Switches

Review:

- VLANs are used to break up broadcast domains; they keep network devices on one VLAN from broadcasting to hosts on another VLAN.  Unless a router is used to route between VLANs, the network devices on one VLAN cannot communicate with devices on another VLAN.

- Switches are programmed for all ports to belong to VLAN 1

- Each VLAN corresponds to a specific network or subnetwork ID

- Trunking is used to carry VLAN information from one switch to another or from one switch to a router.  This means that switch-connected network devices on a specific VLAN can communicate with devices on the same VLAN that connect to another switch.

- A normal Switch port can only belong to one VLAN

- A Trunk port is not a member of any VLAN, but passes all VLAN information to the attached neighboring port

Step-by-Step Instructions:

- Console into the switch and erase both switches.  Connect a crossover cable between the two Ax ports on CAT 1900, or between ports 10x on CAT 2950.

  - What are the commands that you had to use to set the switch to the factory default:_________________________________________________

- Create VLAN 2 and 3 on both switches, and name them Accounting and Admin respectively

  - What were the commands you typed to create and name the VLANs?

________________________________________________________
________________________________________________________

- Assign Port 2 in both switches to VLAN 2, and port 3 in both switches to VLAN 3

  - What were the commands that you used to statically assign ports to VLANs?

_______________________________________________________

_______________________________________________________

  - What is the show command that you used to confirm the ports VLAN membership?

_______________________________________________________

- Configure the Trunk ports on both switches using the following commands:

| 1900 | 2900 |
| --- | --- |
| (config)# int fa 0/26 | (config)#int fa 0/10 |
| (config-if) trunk on | (config-if)#switchport mode trunk |
| #show trunk A | #show int fa 0/10 switchport |

  - Based on the results of the show command answer the following questions:

    - What is the encapsulation type?______________________

    - What is the status of the Trunk(1900)?_________________

    - What is the operational mode of the port (2950)?_________

    - Why can’t we trunk a 1900 switch to a 2950 switch?

________________________________________________

- Configure the stations on VLAN 2 with cable 192.5.2.0/24, and the stations on VLAN 3 with cable 192.5.3.0/24

| VLAN 2 Station (Accounting) | VLAN 3 Station (Admin) |
| --- | --- |
| IP address: | IP address: |
| Subnet Mask | Subnet Mask: |

- Connect one host to SwitchA‘s port 2, and another host to SwitchB’s port 2.  Configure both hosts with the proper IPs that correspond to their VLAN membership.  Send a ping packet from the station on VLAN 2 on SwitchA to the station on VLAN 2 on SwitchB.

  - Was the ping successful?____________________.  If not troubleshoot

  - Why was the ping successful?________________________________

- On SwitchB, move the host cable currently plugged into port 2 to port 3.  Send a ping packet from the station on VLAN 2 on SwitchA to the station on VLAN 3 on SwitchB.

  - Was the ping successful?____________________.  If yes troubleshoot

  - Why was not the ping successful?_____________________________

_____________________Instructor’s Initial