CET 2615C

Semester 3 Skills-Based Final (Passing Grade is 75%)

You are one of the network engineers working for Orange County Public Schools.  You have been assigned the job of connecting one of the high schools to the district office network. The district office router will provide the DCE clocking signal.

At the school end, you decided to create a separate VLAN for students; all school faculty and administrators will be on VLAN 1, and all the students will be on VLAN 2.   The cable ID 219.17.100.0 has been assigned to the school LAN, however knowing the school layout you decided that you need to have four 62-hosts subnets. The first two subnets will be used as follow:

Subnet 0:  VLAN 1 – Faculty and Administrators

Subnet 1: Students

You also decided to reserve the lower range of subnet 0 (219.17.100.1 – 219.17.100.31) to administration, and to dedicate the upper range of subnet 0 (219.17.100.32 – 219.17.100.63) to faculty PCs.

Use the following information and the above diagram to configure the equipment at the school and at the district office.

| District Router DR | School Router SR |
| --- | --- |
| E0: 192.5.5.1 | E0: 219.17.100.1 |
| S0: 199.6.13.1 | S1: 199.6.13.2 |

IP Planning (10 Points):

| Subnet # | Range |
| --- | --- |
| 0 | Admin Range: Faculty Range: |
| 1 |  |
| 2 |  |
| 3 |  |
| Instructor Initials |  |

District Router Configuration (10 Points):

| Task | Instructor’s Initial |
| --- | --- |
| Name the router DR |  |
| Configure E0 |  |
| Configure S0 |  |
| Configure the district router to provide clocking |  |
| Configure IGRP 100 |  |
| Map the host name SR to 219.17.100.1 |  |
| Configure encrypted password |  |
| Configured VTY lines (use password vtypass) |  |

School Router Configuration (10 Points):

| Task | Instructor’s Initial |
| --- | --- |
| Name the router SR |  |
| Configure E0 |  |
| Configure S1 |  |
| Map the host name DR to 192.5.5.1 |  |
| Configure IGRP 100 |  |
| Configure encrypted password |  |

School Switches Configuration (20 Points):

| LAN_SW1 | Instructor’s Initial | LAN_SW2 |  |
| --- | --- | --- | --- |
| Name the switch LAN_SW1 |  | Name the switch LAN_SW2 |  |
| Configure the switch with the domain name School |  | Configure the switch with the domain name School |  |
| Configure the switch to act as the domain server |  | Configure the switch to act as the domain Client |  |
| Configure the switch with IP 219.17.100.2 |  |  |  |
| Enable Trunking on Port A (1900), or port 12 (2950) |  | Enable Trunking on Port A (1900), or port 12 (2950) |  |
| Create VLAN 2 and Name it Students |  |  |  |
| Server Revision # |  | Client Revision # |  |
| Assign ports 7-11 to VLAN 2 |  | Assign ports 7-11 to VLAN 2 |  |

Station1 Configuration (5 Points)

Configure station1 to be a member of VLAN1 (Administration and Faculty).  Assign the station an IP address from the upper range of subnet 0 (Faculty Range).

| Task | Instructor’s Initial |
| --- | --- |
| Station 1 is connected to the correct port on the switch: |  |
| Change the host name to Station1 |  |
| IP address: |  |
| Subnet Mask: |  |
| Default Gateway |  |
| Station1 Can access the http server at the district office LAN |  |
| Station 1 can telnet to the district office |  |

Adding and Testing Security (30 Points)

Adding Security:

The following is a description of the security policy set froth between the school and district office.

- The students can not communicate neither with the faculty nor with the administration

- The students can not communicate with district LAN

- The faculty can only access any web server at the district office.

- All other traffic from the faculty to the district office is denied.

- The administration can access any web server at the district office.

- The administration can also telnet to any device at the central office.

- All other traffic from the administration to the district office is denied.

Use ACL 101 Inbound E0

Testing Security

Configure Station1 to be a member of VLAN1 (Administration and Faculty).  Assign the station an IP address from the upper range of subnet 0 (Faculty Range).

| Task | Instructor’s Initial |
| --- | --- |
| Station1 can access the http server at the district office LAN |  |
| Station1 can not telnet to the district office using the route’s host name |  |
| Station1 cannot ping the http server |  |

Assign the station an IP address from the Lower range of subnet 0 (Admin Range).

| Task | Instructor’s Initial |
| --- | --- |
| Station1 can access the http server at the district office LAN |  |
| Station1 can telnet to the district office using the route’s host name |  |
| Station1 cannot ping the http |  |

Part 2 Troubleshooting (10 Points)

Objective: After your workstations, switches and routers are successfully configured, you will be asked to leave and problems will be introduced to demonstrate troubleshooting skills. Problems encountered during troubleshooting and the steps taken to correct them must be documented. Problems will focus on OSI layers 3 and 4 resulting in loss of network connectivity or causing the ACL not to function correctly. Examples include: 1) Change workstation IP settings, 2) Change router IP / interface configuration, 3) Change the ACL statements, 4) Change the interface or remove the ACL from an interface on the router. 5) Change the routing protocol used.)

| Symptom/Cause | Tests/Results | Detailed Solutions | Initials |
| --- | --- | --- | --- |

Documentation (5 Points):

(Capture and print the configuration files for all equipment (school and district routers, and school switches) Make sure to give your configuration files a unique name so they would not get mixed with the configuration files of other students						      						     Initials________

(All equipment is reset to the factory default at the end of the test.       Initials________