Tokyo-to-Moscow network: 192.168.253.0/24

Tokyo-to-Sydney network: 192.168.254.0/24

Helpful show and Troubleshooting Commands

Show int bri0

Debug isdn q921

Debug dialer events

Isdn call interface bri0/0 ldn

Debug ppp authentication

Show dialer

Tokyo Configuration

(config)#hostname Tokyo

Tokyo(config)#username Moscow password 0 cisco

Tokyo(config)#username Sydney password 0 cisco

interface FastEthernet0/0

Tokyo(config-if)#ip address 192.168.1.1 255.255.255.0

Tokyo(config-if)#no shut

interface BRI0/0

no shut

Tokyo(config-if)#dialer pool-member 1

isdn switch-type basic-ni

isdn spid1 51055512340001 5551234

isdn spid2 51055512350001 5551235

interface Dialer1

description profilel used to connect to the Moscow router

ip address 192.168.253.1 255.255.255.0

encapsulation ppp

dialer pool 1

dialer remote-name Moscow

dialer string 5554000

dialer string 5554001

dialer-group 1

ppp authentication chap

interface Dialer2

description the porfile used to connect to Sydney router

ip address 192.168.254.1 255.255.255.0

encapsulation ppp

dialer pool 1

dialer remote-name Sydney

dialer string 5557000

dialer string 5557001

dialer-group 1

ppp authentication chap

(config)#ip route 192.168.2.0 255.255.255.0 BRI0/0

(config)#ip route 192.168.3.0 255.255.255.0 BRI0/0

(config)#dialer-list 1 protocol ip permit

Moscow Configuration

(config)#hostname Moscow

(config)#username Tokyo password cisco

interface Ethernet0

ip address 192.168.2.1 255.255.255.0

no shut

interface BRI0

no sh

dialer pool-member 1

isdn switch-type basic-ni

isdn spid1 51055540000001 5554000

isdn spid2 51055540010001 5554001

interface Dialer0

description the profile for the connection to Tokoy

ip address 192.168.253.2 255.255.255.0

encapsulation ppp

dialer pool 1

dialer remote-name Tokyo

dialer string 5551234

dialer string 5551235

dialer-group 1

ppp authentication chap

(config)#ip route 0.0.0.0 0.0.0.0 BRI0

(config)#dialer-list 1 protocol ip permit

Sydney Configuration

(config)#hostname Sydney

(config)#username Tokyo password 0 cisco

interface Ethernet0

ip address 192.168.3.1 255.255.255.0

no shut

interface BRI0

no shut

dialer pool-member 1

isdn switch-type basic-ni

isdn spid1 51055570000001 5557000

isdn spid2 51055570010001 5557001

interface Dialer1

description profile used to connect to Tokyo

ip address 192.168.254.2 255.255.255.0

encapsulation ppp

dialer pool 1

dialer remote-name Tokyo

dialer string 5551234

dialer string 5551235

dialer-group 1

ppp authentication chap

(config)#ip route 0.0.0.0 0.0.0.0 BRI0

(config)#dialer-list 1 protocol ip permit