CWNA

Final Exam – Skills

- Reset all equipment before you start

- Interconnect devices as shown in the topology

- Use the following information to configure the network

  - Create an BSS with the following SSID:  group# (all lower case, and no spaces)

  - Network Address:  192.168.(group#).0/24

  - Gateway Address:  192.168.(group#).254/24

  - Cisco AP IP Address:  192.168.(group#).1/24

  - PC Ethernet Card (LAC# 11):  192.168.(group#).(100+PC#)/24

  - PC Wireless Card:  192.168.(group#).(200+PC#)/24

  - Laptops’ Wireless Card Addresses:   192.168.(group#).3/24, and  192.168.(group#).4/24

- Disable the broadcasting of the SSID on the AP

- Use WPA-PSK Authentication with TKIP Encryption on the Cisco AP and on wireless Clients

- Create an IP filter to disable Telnet

Date:______________________________

Group# _____________________________

Name: ______________________________

Name: ______________________________