CET2854C MidTerm Exam

Group Members

1._______________________________	2.__________________________________

3._______________________________	4.__________________________________

Instructions and Configuration Tasks

- Reset all equipment before you start

- Interconnect devices as shown in the topology

- Use the following information to configure the network

  - Create an ESS with the following SSID:  group# (all lower case, and no spaces)

  - Network Address:  192.168.(group#).0/24

  - Gateway Address:  192.168.(group#).254/24

  - Cisco AP IP Address:  192.168.(group#).1/24

  - Linksys AP IP Address:  192.168.(group#).2/24

  - PC Ethernet Card (LAC# 11):  192.168.(group#).(100+PC#)/24

  - PC Wireless Card:  192.168.(group#).(200+PC#)/24

  - Laptops’ Wireless Card Addresses:   192.168.(group#).3/24, and  192.168.(group#).4/24

- Disable the broadcasting of the SSID on both APs

- Use Open Authentication with No Encryption on the Cisco AP and disable security on the Linksys AP

- On the Cisco AP, change the maximum transmit power to 1 or 5 mW and change the data rates to Best Throughput

- Disable the DHCP server on the Linksys AP

- Use the following Channel Assignment:

| Group | Channel |
| --- | --- |
| Group1 | Channels 1, and 2 |
| Group 2 | Channels 3, and 4 |
| Group 3 | Channels 5, and 6 |
| Group 4 | Channels 7, and 8 |
| Group 5 | Channels 9, and 10 |

Note:  Understand that we have total of 10 APs and 10 channels in such a limited area.  Therefore, each group will be working on reducing the coverage area of each AP (creating a Pico Cell) by lowering the transmit power; however, you also want to make sure that the two cells (the Cisco’s and the Linksys’s) can still overlap by at least twenty percent.

- On all wireless cards disable Windows Wireless Zero Configuration and Use the Cisco Aironet Client Utility to configure a profile to connect to your wireless LAN

- What is the signal strength in dBm?
Laptop 1:__________________________
Laptop 2:_____________________________

- What is the noise Level in dBm?
Laptop 1:__________________________
Laptop 2:_____________________________

- Make sure that the two laptops can roam between the two cells.

- Enable internet sharing on one of the PCs.  Keep your private network address (192.168.gourp#.0/24) instead of using the default private network which is 192.168.0.0/24.  Make sure that you configure you internal host with the correct Address of the DNS Server and with the correct Gateway Address.

- From one of the laptops download the free version of Golden FTP from the following web site:  http://www.goldenftpserver.com/download.html .  Install the application and create a root directory on your desktop.  Move the files in the CD on the back of your lab manual to the FTP root directory.

- Make sure that the two laptops are associated to two different APs.

- From the second laptop ftp the folder. What was the throughput in Kilobits per second? _______________________