| Prompt | Mode | Description |
| --- | --- | --- |
| > | User | Restricted Access-You can see (few things), but you can’t touch |
| # | Privileged | You can see everything, and you can branch out to configuration tasks and modes |
| (Config)# | Global Configuration | Your can configure the router specific information such as name and password |
| (Config-if)# | Interface Configuration | Your can configure interface specific information (Ethernet, serial, BRI, etc…) |
| (config-router)# | Router Configuration | Your can configure the router with routing protocol |

Router Configuration Modes

Configuring a Router with Routing Information Protocol (RIP)

- Click on the hyper terminal icon in your task bar

- Answer no to the first question:  What was the question?_______________

- Answer yes to the second question:  What was the question?_____________

- How does the prompt look right now? ________, and what does it mean? You are in ______________________Mode

- Use the command show version to see what router platform you have

- What is your router platform? _________

- What is your current router name?_________________

- Try to use the command show run.  What was the output of that command? ________________________________________________________________, and what does the output mean? ________________

Configure a name for you router by using the following steps in the same sequential order:

- From the user mode use the command enable.  How does the router’s prompt look now? ______________ and what does it mean?  You are in ____________mode.  Were you asked to enter a password to switch into that mode? ____________

- Can you use the command show run now?___________

- Now use the command configure terminal.

- What prompt did the router display?

- What does this prompt mean? _______________

- Now assign a name for your router using the command hostname name.  What change occurred in the prompt?____________________________

- Now, follow the following steps to configure the router with an encrypted password to secure access to the router:

- From the same Configuration mode (which one is that?) use the command enable secret cisco

- Use the command exit. Which configuration mode are you at now_____________?

- Use the command disable.  Which configuration mode are you at now_________________?

- Try to enter privileged mode again using the command enable.  Did a prompt for a password appear?  _______________

- From Privileged mode, use the command show run.  Do you see an encrypted password?____________

Follow the following steps to configure the Ethernet interface of the router:

- From global configuration mode (config)#, use the command interface e0 (for 2500 routers) or interface fa 0/0 (for 2600 routers).

- What prompt did the router display _____________and what does it mean?________________

- From Interface configuration mode (config-if)#, use the command ip address ip address subnet mask (refer to the diagram for IP address assignment).

- From Interface configuration mode, use the command no shutdown.

- Exit out to privileged mode and use the command show interface fa0/0 or e0 (depending on your router platform)

- What is the status of the interface?  Interface is _____ line protocol is _______

- Follow the following steps to configure the serial interface:

- Go to Global configuration mode (config)# and use the following command: interface s0 or interface s1 (for the 2500 routers)
interface s0/0 or interface s0/1 (for the 2600 routers)

- From Interface configuration mode (config-if)#, use the command ip address address mask (refer to the diagram for IP address assignment).

- How many serial interfaces did you have to configure for your router?_________

- From Interface configuration mode, use the command no shutdown.

- If you are configuring Serial 0, then You have to use the following command in interface configuration mode clockrate 56000

- Exit to privileged mode then use the command show ip interface brief. Are all of your interfaces up?_____________________________

- Enable your lowest numbered NIC and configure it according to the diagram.  Also, make sure that your highest numbered NIC is disabled.

- From your work station Ping the default gateway.  Was the ping successful?  If not troubleshoot.

- Ping your other 3 neighbors.  Was the ping Successful?_______________

- If not, Why? ___________________________________

- Go back to your router and use the command show ip route from privileged mode.

- List the networks that your router know how to reach:
___________________________________________
_______________________________________
______________________________________________

Now, let’s teach the router how to get to other networks by configuring Routing Information Protocol (RIP).  Let’s follow the steps together:

- From global configuration mode use the command router rip

- What prompt did the router display _____________and what does it mean?________________

- List the directly attached networks using the network command: 
 network network address.  Repeat the command for each directly attached network.

- How many directly attached networks does your router have? _____________

- From privileged mode use the command show ip route. List all the networks that your router knows how to reach:
_____________________	______________________	_______________
_____________________	____________________	_______________
_____________________	_____________________	________________

- How did your router learn about all these networks?_______________________

- Ping all of your neighbors.  Was the ping successful?____________. If not troubleshoot.