Group Exercise

- Connect your PC to the switch

- Disable LAC#3 and enable LAC#5

- Configure TCP/IP property

  - IP address: 223.10.5.PC#

  - Subnet Mask: 255.255.255.0

  - Default Gateway: N/A

- Use the ipconfig /all utility from DOS to confirm the configuration

- Test connectivity using PING.  Was the test successful __________?  How do you know_____________?

- From your ARP table, record the MAC address of your lab partner.  Remember, to the command arp –a will display your arp table. _______________________

- Open packet tracer and connect 4 workstations to a hub.  Assign IP address to workstations (192.5.5.1-192.5.5.4).

- Go to simulation mode and send a packet from PC0 to PC1.  Was the packet received by all nodes? _____________ Why________________________

- From simulation mode create another packet from PC2 to PC3.  Send the two packets at the same time (from PC0, and from PC2).  Did collusion occur?_______________  Why ______________________

- Delete the hub from the topology and replace it with a switch.

- Congratulations!  You are ready for today’s Listen(