Valencia Community College

Computer Engineering Technology (Networking)

##### Class:  CET 2930C

##### Networking and TCP/IP Fundamentals

Room:  9-208

## Lecturer:  Professor Yousif

# Final Exam Practice

- Which of the following is associated with a MAC address in a switch’s table?

  - Port number

  - IP address

  - Protocol

  - Subnet mask

- What is a connection between two different hubs, switches, or routers called?

  - Mainline

  - Backbone

  - Leadwire

  - Link Source

- Networks enable multiple users to share devices and data that, collectively, are referred to as the networks’______________

  - Devices

  - Resources

  - Data files

  - Peripherals

- The peer to peer network is an example of a ________________

  - Metropolis area network

  - Wide area network

  - Local area network

  - Tiny area network

- Peer-to-peer network require a special network operating system.

  - True

  - False

- The method that says that before a computer starts to send a message it should first “listen” on the cable to see if any other computer is sending a message is called

a.	Token-passing

b.	Demand priority

c.	CSMA/CD

d.	Star

- Which one of the following devices can be used to eliminate collisions?

  - Hub

  - Repeater

  - Switch

  - Router

- Which one of the following devices can be used to reduce broadcast storms?

  - Hub

  - Repeater

  - Switch

  - Router

- A collision domain is defined as all the devices connected through the same port on the router

  - True

  - False

- Broadcast domain is defined as all the devices connected through the same port on the switch

  - True

  - False

- Which one of the following equipment functions on the physical layer of the OSI model?

  - Router

  - Bridge

  - Switch

  - Hub

- In a routing table, the term metric refers to which one of the following:

  - Number of seconds the router needs to reach a particular destination

  - Number of switches the router needs to go through to reach a particular destination

  - Number of routers the router needs to go through to reach a particular destination

  - Number of subnets the router needs to go through to reach a particular destination

- What type of information will an ARP command return?

  - An IP address

  - A socket address

  - An IPX address

  - A MAC address

- Which of the following protocols does PING use to request responses from devices?

  - SNMP

  - SMTP

  - ICMP

  - RARP

- DNS is used to perform which one of the following functions

  - Resolve IP address to MAC addresses

  - Resolve NetBIOS names to IP

  - Resolve Host names to IP

  - Resolve router names to IP

- What provides the highest level of DNS authority?

  - Root servers

  - Core routers

  - Zone servers

  - Backbone servers

- The socket address 204.113.19.80:23 probably belongs to which one of the following services

  - FTP

  - HTTP

  - SNMP

  - Telnet

- If a client’s workstation’s IP address equals 119.55.60.122 and the network administrator is using 4 bits for Subnetting, which of the following is probably the workstation subnet mask.

  - 255.0.0.0

  - 255.240.0.0

  - 255.255.255.16

  - 255.255.255.255

- What is the maximum number of bits that can be borrowed from a class C network?

  - 6

  - 8

  - 24

  - 22

- Given the IP address 156.1.128.200 with a subnet mask of 255.255.255.128, what is the bit mask?

  - 8

  - 24

  - 25

  - 26

- Given the IP address 196.1.128.200 with a subnet mask of 255.255.255.252, what is the number of subnets created?

  - 16

  - 32

  - 64

  - 128

- Given the IP address 196.1.128.200 with a subnet mask of 255.255.255.252, what is the number of hosts created per subnet?

  - 4

  - 8

  - 16

  - 32

- Which one of the following information holds true about logical Anding:

  - 1 And 1 = 2

  - 1 And 1 = 0

  - 1 And 1 = 255

  - 1 And 1 = 1

- Which one of the following is a routing protocol:

  - IP

  - IPX

  - RIP

  - Apple Talk

- Packets are made up of all of the following parts except

a.	data

b.	trailer

c.	header

d.	footer

- The MAC address is ___________ bytes long.

  - 16

  - 8

  - 6

  - 20

- The IP address is _________bytes.

  - 20

  - 32

  - 4

  - 8

- The minimum size of a TCP header if options field is not used is _________bytes.

  - 20

  - 40

  - 50

  - 60

- The IP address 9.146.118.20  is a(n) _____ address.

a.	Class A

b.	Class B

c.	Class C

d.	invalid

- 197 converted to binary is___________

  - 11111111

  - 00001111

  - 11000011

  - 11000101

- 00001111 converted to decimal is______________

  - 255

  - 192

  - 15

  - 17

- Each Class C network can have _____ hosts.

a.	2

- 254

- 65,536

d.	2 million

- A class A IP address follows which one of the following formats

  - N.N.N.H

  - N.N.H.H

  - N.H.H.H

  - H.H.H.N

- Which command produces the following output:

  - Ping

  - Telnet

  - Arp –a

  - TCP

- Which command produces the following output:

  - Ping 198.133.219.25

  - Telnet

  - Arp –a

  - TCP

- TCP/IP works on the principle that each computer on the network has a unique IP address.

  - True

  - flase

- If a client’s workstation’s IP address equals 119.55.60.122 and the network administrator is using 1 octet for Subnetting, which of the following is probably the workstation subnet mask.

  - 255.0.0.0

  - 255.255.0.0

  - 255.255.255.0

  - 255.255.255.255

- Which top-level domain would the U.S. Congressional offices use?

  - .loc

  - .com

  - .edu

  - .gov

- Although DHCP enables users to move their machines from one location in the network to another without reconfiguring TCP/IP settings, what might a user have to do once he/she has moved to a new part of the network so as to connect to the network and use TCP/IP applications?

  - Change her primary DNS settings

  - Change her default protocol settings

  - Release and renew her IP address

  - Adjust the time on her DHCP lease

- If you know that your boss’s TCP/IP host name is JSMITH, and you need to find out what her IP address is, what command should you type at your DOS prompt?

  - nslookup jsmith

  - Netstat jsmith

  - Tracert jsmith

  - Whois jsmith