Configuring Telnet on Windows 2000 Server

Objectives:

In this lab you will configure Telnet Services on a Windows 2000 sever.  You will then telnet into the server and manage it remotely.

Step 1:  Start the Telnet service on your windows 2000 server

Go to start> programs > administrative tools.  After the computer management window displays on screen, click the plus (+) symbol to the left and select services from the expanded tree.

The services section contains controls for starting and stopping the various services that are run in windows 2000.

To start the telnet service, right-click the service and select start form the menu.  A status indicator displays as Windows attempts to start the service.  Check the status column and verify that the service started.

Step 2:  Telnet to the Windows 2000 server

Ask your neighbor to telnet to your server, meanwhile you can also telnet to your neighbor’s server.  Here are the steps:  (Before you start on this step make sure that you start capturing packets with ethereal)

Go to Start>Run and enter telnet ip_address or telnet  hostname. (This should be the ip address or the name of the remote server that you are trying to telnet to) When asked for a username use “administrator”, and when asked for password use “password”.

The DOS prompt at the remote host will open and now the system can be manipulated remotely.

Step 3:  manipulating a Windows 2000 server remotely through a telnet session

From the DOS prompt C:\> use the command ipconfig  /all and record the following:

Host Name:_____________________________________

IP Address:______________________________________

To which host does this information belong?  Does it belong to the local host or to the remote host?  ____________________________________

Now!  Let’s stop the FTP services on the remote host by using the command net stop msftpsvc.

Open your browser and try to FTP to your neighbor’s ftp server as you did before in the FTP lab.

Were you able to access your neighbor’s FTP server____________?  Why not_____________?

At this Time your neighbor has also stopped the FTP services running in your server.  
Go to System Services window as you did earlier (refer back to the first paragraph in step #1).  Find the FTP service.  Is the service still running or was it stopped? _____________

Reflection

- IS telnet service enabled by default on Windows 2000 server? ______________
Why?___________________________________________________________

- What is the telnet service used for? ____________________________________________________________________________________________________________________________________

- Telnet is at which layer of the TCP/IP model?_____________________________