CallManager Basic Configurations

- Login to Cisco CallManager Administration.  User name is “Administrator”, and password is “password”.

- Click on the details Command button and record the following information:

  - CallManger system version:___________________________

  - Server:______________________________

  - Database:_______________________________

- From programs choose Microsoft SQL Server, then select Enterprise Manger

- Click the + sign to the left of the Microsoft SQL servers, and then select SQL Server Group.  Choose the Local server, and then click on the databases folder.

  - What is the current database? __________________________________

Notice that the first database installed will always be CCM0300

- Expand the current database to verify the server’s function

  - Is this a subscriber of a publisher database? ______________________

Notice that CallManager publisher will have a publications folder in the database while a CallManger subscriber will have a pull subscription folder in the database

- Close the SQL Enterprise Manager

- Go to the system menu, then select server and change the server name to an IP address depending on your Pod number.  When done, click update.

- Select Cisco CallManger from the system menu.  Change the server name to the proper IP address depending on your Pod number.

- Go down to the auto registration information and configure your directory number information depending on your Pod number.  When done, click update.

- In about two minutes, phones should register with the CCM.  If after two minutes phones still did not register then you may need to restart the CallManger Service.

- To restart the service, go to “start” Menu choose “programs”( “Administrative Tools” ( “Services” ( “Cisco CallManager” and restart the service.

- If your phone still has not registered, you might need to erase the configuration of your phone.  Refer to the Network Configuration lab for step-by-step instructions.

- Go to the device Menu, then select phone and check on the phones registration

- Place a call from one extension to another.

- On the CallManger server click start, programs, administrative tools, then performance.

- Click the + icon on the tool bar.  Under performance object select Cisco CallManger. In performance monitor, select the following counters.

  - Number of calls in progress

  - Number of calls completed

  - Number of call attempts

The following is an example of how your screen should look.

- Leave the performance window running then attempt to make calls again.  Now click on the report icon on the performance screen.  You should be able to get a similar screen to the one below.

  - What is the number of Active Calls? _____________________

  - What is the number of Attempted Calls? ______________________

  - What is the number of calls in progress? ____________________