Changing the IP Address of the CM Server

- Make sure that your Headset is connected.

- Go to the TCP/IP properties of the Win 2K server and change the IP address according to your Pod number.

- From the System menu change the IP address of the CM server

- Go to the DHCP service  and delete the old Scope (192.168.1.0/24)

- Create a new Scope (pool of IP addresses depends on your pod number)

- Configure DHCP options 028, 042, 066.  The IP address for all those should be the same as the IP address for the CM Server.

- Restart Win 2K.  Make sure that you do not shut the server down.  If you do by mistake, you will lose all the changes you made.

- Delete all the phones from the standard image

- Switch the client(s) to DHCP

- For more information on changing the IP address of Cisco CM go to: http://cisco.com/en/US/products/sw/voicesw/ps556/products_tech_note09186a0080094601.shtml