Network Configurations

- Change the IP address of the server where CCM is running

  - Select Local Area Connection number 1 “LAC” and change the TCP/IP properties according to the lab1 setup.

  - Check on your configuration with the ipconfig /all utility

- Configure DHCP Services on the server running CCM

Create a new scope

Specify the range of available IP addresses.  Make sure that the length of the bit mask is 24

Move forward to configuring options and configure the IP address of the default gateway.  The default gateway usually gets the first available IP address on the network.  Even though a default gateway is not configured at this time, it will be configured in future meetings.

- Configure TFTP Option

Select “Configure Options” from the Action menu

Configure option 066

- Configure Network Time Protocol Option 042

- Verify Configuration on the IP phones

  - Press **# to unlock the configuration “nothing will change on the display”

  - Press the settings key. Scroll down to Network Configuration and press the select key.

  - Dial 33 to go to the Erase Configuration option.  Press the Yes Softkey then press save then Exit.

  - The phone now will start to acquire the new network configurations

  - When your phone is done reloading, press the settings button and go to network configuration.  Move down through the settings and record the following:

    - DHCP Server:________________________

    - Host Name:_____________________________

    - IP Address:____________________________

    - MAC Address:_________________________

    - TFTP Server: ___________________________

    - Call Manager:___________________________

  - Press the cancel Softkey when done.  Note that at this point the IP phone is not fully configured; the process will be complete after the CCM is configured.

- Verify the registration of the IP phones with the DHCP server

- Configure and Use Remote Desktop