Bulk Administration Tool (BAT)

Installation and Configuration

- From Cisco CallManager Administration, go to the Application menu ( Install Plug-in ( Cisco Bulk Administration Tool.

- Download the application to the C Drive.  When the download is complete, install the application.  Go back to the Application menu.  Do you see BAT listed as a choice under this menu? ___________ IF not, troubleshoot.

- Start BAT, and create a new template for the IP phones by taking the following steps:

  - From the Configure Menu, choose Template ( Phone

  - In the Phone Template Configuration Page change the Phone Template Name to Pod#_Template; change the Device Type to Cisco 7960; set the Device Pool to Default; scroll down to the “Phone Button Template and Expansion Module Template Information” section and select Standard 7960 for the Phone Button Template

  - When done, click on Insert.

- To add two lines to the phone template, scroll to the bottom and click on Line 1 then click on Insert and Close.  Repeat the same steps for Line 2.

- From the CallManager hard drive, go to c://ciscowebs/BAT/ExcelTemplate.

- Share the ExcelTemplate folder, and ask your lab partner (who is not running CM) to access the folder and copy the file “bat.xlt” to his desktop.

- From your lab Partner’s PC, open MS Excel and go to the Tools Menu ( Macro ( Security ( set the security level to Medium.

- Close Excel then open the bat.xlt file

- Populate the following fields:

  - Set the number of phone lines to 2 and the number of speed dials to 4.

  - Enter the MAC address of the phone(s)

  - Enter the number for directory numbers 1, and 2 (Lowest DN + 11/12)

  - Configure the display for the two lines

  - Configure the description as BAT Phone

  - When done, click on the Export to BAT Format.  Save the file to a newly created directory under the C Drive.  Name the folder:  BAT_Files, and name the file BAT_7960.

- Close MS Excel.  When asked to save the file, select Yes.  Save the file to a newly created directory under the C drive.  Name the folder BAT_Excel_Files, and name the file BAT_Excel_7960.

- Share the BAT_Files directory.  From CM, access the shared “BAT_Files” Directory.  Copy the “BAT_7960” file to the following directory in CM:  C:/batfiles/phones/insert.

- Since you cannot register a phone using BAT if it has already been registered using Auto-Registration, you will have to delete the phones first before using BAT registration.  To do so, go the Device menu from the CallManager Administration and select Devices ( Phones, then click on the find button.  Check all the phones that you want to delete then click on the delete button.

- In this step, you will import the Database to BAT.  To do so, from the BAT Administration page go to the Configure menu, then select Phones.  Configure the following fields:

  - File Name:  BAT_7960

  - Phone Template Name:  Pod#_Template

  - Model:  Cisco 7960

- When done, click on Validate.  When Validation is complete, click on Insert.

- To Verify the BAT Registration, Select Phones from the Devices menu, then click on the Find Button.  Did the BAT phone show up in the list __________?  If not, troubleshoot.