05/23/2005 12:47:01.874 CCM|StationInit - InboundStim - KeepAliveMessage - Send KeepAlive to Device Controller. DeviceName=SEP000F8F59D304, TCPHandle=000000004, IPAddr=192.168.1.128, Port=52952, Device Controller=[1,92,1]|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.984><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:16.906 CCM|StationInit - InboundStim - KeepAliveMessage - Send KeepAlive to Device Controller. DeviceName=SEP000BDBDF827D, TCPHandle=000000005, IPAddr=192.168.1.240, Port=1046, Device Controller=[1,92,2]|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.986><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:17.397 CCM|StationInit: 000000004 OffHook.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 StationOutputDisplayText don't need to send, because mIsALegacyDevice = 0|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><MN::Directory Number><MV::40000><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 SetRinger ringMode=1(RingOff).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 SetLamp stimulus=9(Line) stimulusInstance=1 lampMode=2(LampOn).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 CallState callState=1 lineInstance=1 callReference=16777225|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 DisplayPromptStatus timeOutValue=0 promptStatus='€ ' content='Enter Number' lineInstance=1 callReference=16777225 ver=0x80000004.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 SelectSoftKeys instance=1 reference=16777225 softKeySetIndex=4 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.397 CCM|StationD:    000000004 ActivateCallPlane lineInstance=1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:17.407 CCM|StationD:    000000004 StartTone tone=33(InsideDialTone), direction=0.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.987><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:19.200 CCM|StationInit: 000000004 KeypadButton kpButton=4.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.989><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:19.210 CCM|StationD:    000000004 StopTone.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.989><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:19.210 CCM|StationD:    000000004 SelectSoftKeys instance=1 reference=16777225 softKeySetIndex=6 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.989><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:20.842 CCM|StationInit: 000000004 KeypadButton kpButton=0.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.990><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:21.203 CCM|StationInit: 000000004 KeypadButton kpButton=0.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.991><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:21.513 CCM|StationInit: 000000004 KeypadButton kpButton=0.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.992><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.084 CCM|StationInit: 000000004 KeypadButton kpButton=4.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><MN::Directory Number><MV::40000><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000004 SelectSoftKeys instance=1 reference=16777225 softKeySetIndex=8 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><MN::Directory Number><MV::40004><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 StationOutputDisplayText don't need to send, because mIsALegacyDevice = 0|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 CallState callState=4 lineInstance=1 callReference=16777226|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 CallInfo callingPartyName='Wael Yousif' callingParty=40000 cgpnVoiceMailbox= 				calledPartyName='' calledParty=40004 cdpnVoiceMailbox= 				originalCalledPartyName='' originalCalledParty=40004 originalCdpnVoiceMailbox= originalCdpnRedirectReason=0 				lastRedirectingPartyName='' lastRedirectingParty=40004 lastRedirectingVoiceMailbox= lastRedirectingReason=0 				callType=1(InBound) lineInstance=1 callReference=16777226. version: 0x80000004|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD::star_StationOutputCallInfo(): callInfo: CI=16777226, CallingPartyName=Wael Yousif,  CallingParty=40000, CalledPartyName=, CalledParty=40004, OriginalCalledPartyName=, OriginalCalledParty=40004, lastRedirectingPartyName=, lastRedirectingParty=|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 SetLamp stimulus=9(Line) stimulusInstance=1 lampMode=5(LampBlink).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 SetRinger ringMode=2(InsideRing).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 DisplayPriNotify timeOutValue=10 pri=5 notify='€40000' content='From 40000' ver=-2147483644.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 DisplayPromptStatus timeOutValue=0 promptStatus='€40000' content='From 40000' lineInstance=1 callReference=16777226 ver=0x80000004.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000005 SelectSoftKeys instance=1 reference=16777226 softKeySetIndex=3 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><MN::Directory Number><MV::40000><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000004 CallState callState=12 lineInstance=1 callReference=16777225|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000004 CallInfo callingPartyName='Wael Yousif' callingParty=40000 cgpnVoiceMailbox= 				calledPartyName='' calledParty=40004 cdpnVoiceMailbox= 				originalCalledPartyName='' originalCalledParty=40004 originalCdpnVoiceMailbox= originalCdpnRedirectReason=0 				lastRedirectingPartyName='' lastRedirectingParty=40004 lastRedirectingVoiceMailbox= lastRedirectingReason=0 				callType=2(OutBound) lineInstance=1 callReference=16777225. version: 0x80000004|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD::star_StationOutputCallInfo(): callInfo: CI=16777225, CallingPartyName=Wael Yousif,  CallingParty=40000, CalledPartyName=, CalledParty=40004, OriginalCalledPartyName=, OriginalCalledParty=40004, lastRedirectingPartyName=, lastRedirectingParty=|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000004 DialedNumber dialedNumber=40004 lineInstance=1 callReference=16777225.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.094 CCM|StationD:    000000004 StartTone tone=36(AlertingTone), direction=0.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.104 CCM|StationD:    000000004 CallState callState=3 lineInstance=1 callReference=16777225|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.104 CCM|StationD:    000000004 SelectSoftKeys instance=1 reference=16777225 softKeySetIndex=8 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.104 CCM|StationD:    000000004 DisplayPromptStatus timeOutValue=0 promptStatus='€' content='Ring Out' lineInstance=1 callReference=16777225 ver=0x80000004.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.104 CCM|StationD:    000000004 CallInfo callingPartyName='Wael Yousif' callingParty=40000 cgpnVoiceMailbox= 				calledPartyName='' calledParty=40004 cdpnVoiceMailbox= 				originalCalledPartyName='' originalCalledParty= originalCdpnVoiceMailbox= originalCdpnRedirectReason=0 				lastRedirectingPartyName='' lastRedirectingParty=40004 lastRedirectingVoiceMailbox= lastRedirectingReason=0 				callType=2(OutBound) lineInstance=1 callReference=16777225. version: 0x80000004|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:22.104 CCM|StationD::star_StationOutputCallInfo(): callInfo: CI=16777225, CallingPartyName=Wael Yousif,  CallingParty=40000, CalledPartyName=, CalledParty=40004, OriginalCalledPartyName=, OriginalCalledParty=40004, lastRedirectingPartyName=, lastRedirectingParty=|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.993><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:29.475 CCM|StationInit: 000000005 SoftKeyEvent softKeyEvent=11(Answer) lineInstance=1 callReference=16777226.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 SetSpeakerMode speakermode=1(On).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 ClearNotify.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 SetRinger ringMode=1(RingOff).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 SetLamp stimulus=9(Line) stimulusInstance=1 lampMode=2(LampOn).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 CallState callState=1 lineInstance=1 callReference=16777226|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.475 CCM|StationD:    000000005 ActivateCallPlane lineInstance=1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.995><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.495 CCM|StationD:    000000004 StopTone.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,9.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000004 OpenReceiveChannel conferenceID=0 passThruPartyID=1000091 millisecondPacketSize=20 compressionType=4(Media_Payload_G711Ulaw64k) qualifierIn=?.   myIP: 8001a8c0 (192.168.1.128)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,9.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000005 StopTone.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000005 OpenReceiveChannel conferenceID=0 passThruPartyID=10000a1 millisecondPacketSize=20 compressionType=4(Media_Payload_G711Ulaw64k) qualifierIn=?.   myIP: f001a8c0 (192.168.1.240)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000005 StopTone.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000005 CallState callState=5 lineInstance=1 callReference=16777226|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.495 CCM|StationD:    000000005 CallInfo callingPartyName='Wael Yousif' callingParty=40000 cgpnVoiceMailbox= 				calledPartyName='' calledParty=40004 cdpnVoiceMailbox= 				originalCalledPartyName='' originalCalledParty=40004 originalCdpnVoiceMailbox= originalCdpnRedirectReason=0 				lastRedirectingPartyName='' lastRedirectingParty=40004 lastRedirectingVoiceMailbox= lastRedirectingReason=0 				callType=1(InBound) lineInstance=1 callReference=16777226. version: 0x80000004|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD::star_StationOutputCallInfo(): callInfo: CI=16777226, CallingPartyName=Wael Yousif,  CallingParty=40000, CalledPartyName=, CalledParty=40004, OriginalCalledPartyName=, OriginalCalledParty=40004, lastRedirectingPartyName=, lastRedirectingParty=|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000005 SelectSoftKeys instance=1 reference=16777226 softKeySetIndex=1 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000005 DisplayPromptStatus timeOutValue=0 promptStatus='€' content='Connected' lineInstance=1 callReference=16777226 ver=0x80000004.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000004 StopTone.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000004 CallState callState=5 lineInstance=1 callReference=16777225|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000004 CallInfo callingPartyName='Wael Yousif' callingParty=40000 cgpnVoiceMailbox= 				calledPartyName='' calledParty=40004 cdpnVoiceMailbox= 				originalCalledPartyName='' originalCalledParty= originalCdpnVoiceMailbox= originalCdpnRedirectReason=0 				lastRedirectingPartyName='' lastRedirectingParty=40004 lastRedirectingVoiceMailbox= lastRedirectingReason=0 				callType=2(OutBound) lineInstance=1 callReference=16777225. version: 0x80000004|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD::star_StationOutputCallInfo(): callInfo: CI=16777225, CallingPartyName=Wael Yousif,  CallingParty=40000, CalledPartyName=, CalledParty=40004, OriginalCalledPartyName=, OriginalCalledParty=40004, lastRedirectingPartyName=, lastRedirectingParty=|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000004 SelectSoftKeys instance=1 reference=16777225 softKeySetIndex=1 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.505 CCM|StationD:    000000004 DisplayPromptStatus timeOutValue=0 promptStatus='€' content='Connected' lineInstance=1 callReference=16777225 ver=0x80000004.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,10,10.1><IP::><DEV::>

05/23/2005 12:47:29.515 CCM|StationInit: 000000004 OpenReceiveChannelAck Status=0, IpAddr=0x8001a8c0, Port=17198, PartyID=16777361|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.996><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:29.515 CCM|StationD:    000000005 StartMediaTransmission conferenceID=0 passThruPartyID=10000a1 remoteIpAddress=8001a8c0(192.168.1.128) remotePortNumber=17198 milliSecondPacketSize=20 compressType=4(Media_Payload_G711Ulaw64k) qualifierOut=?.  myIP: f001a8c0 (192.168.1.240)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.996><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:29.525 CCM|StationInit: 000000005 OpenReceiveChannelAck Status=0, IpAddr=0xf001a8c0, Port=24600, PartyID=16777377|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.997><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:29.525 CCM|StationD:    000000004 StartMediaTransmission conferenceID=0 passThruPartyID=1000091 remoteIpAddress=f001a8c0(192.168.1.240) remotePortNumber=24600 milliSecondPacketSize=20 compressType=4(Media_Payload_G711Ulaw64k) qualifierOut=?.  myIP: 8001a8c0 (192.168.1.128)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.997><IP::192.168.1.240><DEV::SEP000BDBDF827D>

05/23/2005 12:47:31.878 CCM|StationInit - InboundStim - KeepAliveMessage - Send KeepAlive to Device Controller. DeviceName=SEP000F8F59D304, TCPHandle=000000004, IPAddr=192.168.1.128, Port=52952, Device Controller=[1,92,1]|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.998><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationInit: 000000004 OnHook.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 CloseReceiveChannel conferenceID=0 passThruPartyID=1000091.  myIP: 8001a8c0 (192.168.1.128)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 StopMediaTransmission conferenceID=0 passThruPartyID=1000091.  myIP: 8001a8c0 (192.168.1.128)|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 SetSpeakerMode speakermode=2(Off).|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 ClearPromptStatus lineInstance=1 callReference=16777225.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 CallState callState=2 lineInstance=1 callReference=16777225|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 SelectSoftKeys instance=0 reference=0 softKeySetIndex=0 validKeyMask=-1.|<CLID::StandAloneCluster><NID::192.168.1.140><CT::1,100,93,1.1000><IP::192.168.1.128><DEV::SEP000F8F59D304>

05/23/2005 12:47:44.987 CCM|StationD:    000000004 DisplayPromptStatus timeOutValue=0 promptStatus='€