VoIP -- Midterm Exam

Instructions:

- Network ID = 200.0.0.0/24

- Gateway Address:  200.0.0.1/24

- CM Address: 200.0.0.100

- Disable auto registration on CM.

- Register phone 1 using BAT.  Phone one should have two lines and 1 speed dial to phone 2.  The two DNs for phone 1 should be 5000, and 5001.

- Register the CIPC phone using manual registration. The DN for phone 2 is 5002.

( Your check point at this time should be that phones 1, and 2 should be able to call each other

- Configure the H.323 voice gateway and register it with CM

- Configure the FXS ports on the router with dial patterns to simulate the connection to PSTN:

  - Phone 3 dial pattern:  4073205555

  - Pone 4 dial pattern:  14086781000

(  Your check point at this time should be that the two PSTN phones should be able to talk to each other.

- Configure Call routing in CM so company XYZ can call the PSTN phones

- Configure the voice gateway with a route pattern so calls can be made from the PSTN to Company XYZ using the company’s Direct Inward Dialing (4075825000-5100)

- Configure a router filter that would allow Local calls only out the h.323 voice gateways.

- Configure partitions and calling search spaces so only phone 1 can make calls to both PSTN and company XYZ phones while phone 2 can make calls to other company XYZ’s phones only.

Student Name: ______________________________________

Student Name: ______________________________________

Instructor’s Signature: ___________________________

# Text boxes

1

2

3

4

XYZ Company