Basic Access-Point Setup Commands

- A student from each group will console to the AP and Reset the AP back to factory default.  This is a two-step process:

  - From global configuration mode use the command “erase start”.

  - When the erase is complete use the command “reload”

- Connect the AP and the clients to the same switch using straight thru cables.

- Configure the AP and the clients with the proper TCP/IP properties as follows:

  - Configure the Bridge Virtual Interface (BVI):  From Interface bvi1 mode use the command ip address 20R#.0.0.3 255.255.255.0

  - Configure the fast Ethernet interface on the AP:  from interface f0 interface configuration mode use the command ip address 20R#.0.0.1 255.255.255.0.  Press return then use the command no shut

  - Configure the TCP/IP properties on the clients starting with 20R#.0.0.11/24.  Now all clients can access the AP via the web interface or a telnet session.

  - Configure the radio interface on the AP:  from interface dot11radio0 interface configuration mode use the command ip address 20R#.0.0.2 255.255.255.0.  Press return then use the command no shut

- Use the following steps to configure the AP with IOS-DHCP

  - From global configuration mode use the command ip dhcp pool rack# (where rack# is the name of the pool). Press enter which will take you to dhcp subconfiguration mode, from there use the command network 20R#.0.0.0 255.255.255.0.  Press enter then use the command default-router 20R#.0.0.10

  - Exit out to global configuration mode, then use the command ip dhcp excluded-address 20R#.0.0.1 20R#.0.0.10

  - This dhcp pool will be used to dynamically assign IP address to clients that will associate with that particular AP.

- Configure the access point with a name

  - From global configuration mode use the command “hostname” followed by the name that you want to assign to the AP.  For example, using the command “hostname ap2” assigns the ap2 name to that particular access point

- Configure the AP with a SSID:

  - From interface dot11radio 0 use the command ssid rack#.  Press enter then use the command guest-mode.  Press enter then use the command authentication open.  Press enter then use the command max-associations 24.

- Exit all the way to privileged mode and save your configurations using the command copy run start

- Enable your wireless card and check to see if you were associated to the AP.  From the command prompt use the command Ipconfig /all to see if you were able to obtain and IP address form the AP.